PRE-USE INSPECTION FORM (TR-F-27B)       Revised 7/09     THESE ITEMS TO BE INSPECTED BEFORE PUTTING VEHICLE IN SERVICE!

SCHOOL DISTRICT NAME __________________________________  LICENSE PLATE # _______________________

MAKE OF BODY ____________________________________ MAKE OF CHASSIS _____________________________

VEHICLE YEAR ________VEHICLE TYPE:  BUS:  TYPE  A ____ B ____ C ____ D ____MULTI-PURPOSE _______

FUEL TYPE:  DIESEL ____ GAS ____ ALTERNATIVE FUEL ____ (SPECIFY ALT. FUEL TYPE)________________

VEHICLE: RATED CAPACITY ______  GVWR ___________ VIN __________________________________________

| 1. AIR CLEANER: furnished & installed properly |  |  | 23: CHILD CHECK MONITOR: installed and operational |  |
| --- | --- | --- | --- | --- |
| 2. ALTERNATOR: A, B,C,&D buses – minimum 130 amps |  |  | 24. SHOCK ABSORBERS: double acting front & rear * |  |
| 3. BACKUP ALARM (meeting SAE J994B) minimum 112dBA* |  |  | 25. SPRINGS/SUSPENSION: * |  |
| 4. BATTERY SYSTEM: 12 volt tested at 0 degree F |  |  | a. Rear Springs--Leaf Type progressive or multistage |  |
| a. Gas Engine: (less than 10,000 lbs GVWR) |  |  | b. Front Springs--Leaf Type, wrapped, one stationary eye |  |
| 125 Min Reserve & 450CCA. Capacity: |  |  | 26. SUN SHIELD * |  |
| b. Gas Engine: (greater than 10,000 lbs GVWR) |  |  | 27. THROTTLE Mechanical or Electric Locking (Type C & D) |  |
| 150 Min Reserve & 500CCA. Capacity: |  |  | 28. WINDSHIELD WIPERS/WASHERS: * |  |
| c. Diesel Engine: (ALL) |  |  | 29. CROSSING GATE: (Not required Type A-II or D) |  |
| 200 min reserve & 1000 CCA. Capacity |  |  | a. Operates with stop arm system |  |
| d. Battery Hold Downs: |  |  | b. Arm 70” when extended (minimum) |  |
| e. Battery Compartment: top surface area non-conductive |  |  | c. Quick disconnect feature for removal |  |
| 5. BRAKES: |  |  | d. Pressure sensitive reverse feature |  |
| a. Service Brakes: functioning * |  |  | e. Single cycle interrupt switch at driver’s console |  |
| b. Emergency Brakes: functioning * |  |  | 30. DEFROSTERS * |  |
| c. Parking Brakes: functioning * |  |  | 31. HEATERS: (Front & Rear) * |  |
| d. All Brake Warning Lights & Alarms Operational |  |  | 32. SERVICE DOORS/EMERGENCY EXITS |  |
| (air & hydraulic brake systems) |  |  | 33. VANDAL LOCKS FUNCTIONING: Optional |  |
| e. Air Dryer: (when applicable) meets or exceeds Bendix |  |  | 34. DRIVER’S SEAT: * |  |
| Model AD9 with heater, self purging |  |  | a. Secured with nuts, bolts & washers |  |
| f. Automatic Slack Adjusters: (all air systems) |  |  | b. High back design |  |
| g. Air Compressor: (when applicable) min. 12.0 CFM/Minute |  |  | c. Back adjusts minimum 15 degrees |  |
| 6. FRONT BUMPER: installed * |  |  | d. Multi-position adjustment by driver |  |
| 7. REAR BUMPER: installed * |  |  | e. Lap belt/shoulder harness |  |
| 8. TOW HOOKS: |  |  | 35. TUBELESS/RADIAL TIRES: (Required) * |  |
| a. 14,500 lbs GVWR or greater (2-required-front) |  |  | 36. UNDERCOATING on underside of metal body panels |  |
| b. Rear toe hooks required-all models |  |  | 37. DOCUMENT COMPARTMENT: |  |
| 9. CLUTCH: Starter interlock switch installed & working |  |  | 38. EMERGENCY EQUIPMENT: |  |
| 10. DRIVE SHAFT: One metal guard per section |  |  | a-1. First aid kit * a-2. Disposable body fluid kit * |  |
| 11. EXHAUST |  |  | b. Fire extinguisher (minimum 2A10BC rating) * |  |
| a. Exits at rear-flush with rear bumper * |  |  | c. Triangular reflectors |  |
| b. Left side exit-18” or less fwd of wheel housing front edge |  |  | d. Webbing cutter (driver accessible) * |  |
| c. Left side exit-does not extend beyond body side |  |  | e. All emergency equipment secured * |  |
| d. 15,000# & > GVWR-does not exit beneath fuel fill or doors |  |  | 39. AUX. FANS (2 mounted) type B,C,&D buses |  |
| 12. FUEL TANK: secure, crash barrier installed * |  |  | 40. HEATERS: (body manuf. installed with name/spec. plate) * |  |
| 13. HEAD LIGHTS: hi/low features * |  |  | 41. HEATER HOSES SPECURED/GUARDED |  |
| 14. HORNS: dual horns, operating * |  |  | 42. A/C UNIT PROPERLY INSTALLED(if equipped) |  |
| 15. GAUGES & INDICATOR LIGHTS |  |  | 43. SCHOOL I.D. SIGNS PROPER SIZE * |  |
| a. Speedometer * |  |  | 44. LAMPS AND SIGNALS: |  |
| b. Odometer * |  |  | a. Headlights (high/low beam) DRL system required * |  |
| c. Air (air brakes) |  |  | b. Clearance lights (2 amber front/2 red rear) |  |
| d. Vacuum (hydraulic brakes) or low vac. warning lights |  |  | c. Intermediate side marker lamp (2-one on each side at mid-pt) |  |
| e. Voltmeter |  |  | d. Backup lights: (Type A=4” min, Types B,C,D=7” min) * |  |
| f. Oil pressure gauge * |  |  | e. Stop/Tail Lights, rear (Service brake activated) * |  |
| g. Water temp. gauge * |  |  | 2—7” inside turn signals (upper) |  |
| h. Fuel gauge * |  |  | 2—4” between belt line & floor line on ea.side of emerg door |  |
| i. Turn signal indicators * |  |  | Type A-II – manuf. standard stop/tail lamps |  |
| j. Headlamp-high beam indicator * |  |  | f. License plate lamp * |  |
| k. Glow plug indicator (diesel engine) |  |  | g. Step well lights (services door operated switch) |  |
| 16. REFLECTORS (Securely Attached 30”-42” from ground) |  |  | h. Supervisor’s light-rearmost ceiling light, separate switch |  |
| a. 2 amber--one back of door entrance rt.side, lt.side-same loc. |  |  | i. Ceiling lights * |  |
| b. Vehicles over 30 ft long-2 amber at mid-pt between f & r ref |  |  | j. Driver’s dome light, separate switch |  |
| c. 2 red--one on each side of body |  |  | k. Instrument panel lights, rheostate controlled |  |
| d. 2 red--one on each side of rear |  |  | l. Strobe light indicator |  |
| 17. STOP ARM/STOP ARM LAMPS |  |  | m. Step well lamp |  |
| 18. STROBE LIGHT |  |  | n. turn signals- amber side mounted, type A,B,C,&D buses |  |
| 19. MUD FLAPS (front & rear) Rubber |  |  | 45. WARNING LAMPS: a. (2 amber & 2 red front and rear) |  |
| 20: RUB RAILS |  |  | b. pilot lights (1 amber, 1 red) |  |
| 21. SEATS: secured properly * |  |  | 46. MIRRORS: a. Interior * |  |
| 22: ROOF HATCHES/EMERGENCY EXITS: |  |  | b. Rear view (outside) (heated) * |  |
| a. 0 to 42 passenger, 1 exit per side & 1 roof hatch |  |  | c. Cross over mirrors in place, secure (heated) |  |
| b. 43 to 78 pass., 2 exits per side & 2 roof hatches |  |  | 47. MASTER WIRING DIAGRAM SUPPLIED |  |
| c. 79 to 90 pass., 3 exits per side & 2 roof hatches |  |  |  |  |
| d. Alarms: (window & hatch), installed and operational |  |  | SIGNATURE __________________________________________ |  |
|  |  |  | INSPECTION DATE ____________________________________ |  |

# NOTE:  * ITEMS PERTAIN TO FAMILY TYPE/MULTIPURPOSE VEHCILES

PLEASE RETURN A PHOTOCOPY OF THE COMPLETED FORM TO: SCHOOL TRANSPORTATION, DEPT OF EDUCATION, GRIMES STATE OFFICE BLDG, DES MOINES, IA 50319-0146 or FAX A COPY TO 515-281-6548